## Contents

## Benefits of this Library
The library was intended to satisfy the following primary goals:
- Support parsing of all common host and ipv4/ipv6 address formats in usage plus some additional formats (see below or see javadoc for the IPAddressString class for the extensive list)
- Support both the parsing and representation of subnets, either those specified by network prefix length or those specified with ranges of segment values. For example, all strings in the list below represent the same IPv4 subnet:
  - with CIDR network prefix length:1.2.0.0/16
  - with mask: 1.2.0.0/255.255.0.0
  - wildcard segments: 1.2.*.*
  - range segments: 1.2.0-255.0-255
  - range using inet_aton format: 0x1.0x2.0x0-0xffff
  - SQL-style single wildcards to end segments: 1.2.___.___
  - IPv4 mapped IPv6: ::ffff:1.2.0.0/112
- Allow the separation of address parsing from host parsing. In some cases you may have an address, in others you may have a host name, in some cases either one, so this supports all three options (for instance, when validating invalid input "1.2.3.a" as an address only, it will not be treated as a host with DNS lookup attempted in the way that InetAddress.getByName does)
- Allow control over which formats are allowed, whether IPv4/6, or subnets, or inet_aton formats, and so on.
- Support the production of collections of valid IPv4 and IPv6 address strings of different formats for a given address.
  Some addresses can have hundreds of thousands of potential string representations (when you consider hex capitalization, ipv6 compression, and leading zeros, the various IPv4 and IPv6 formats, and combinations of all the above), although there are generally a handful of commonly used formats. Generating these strings, whether the handful of commonly used strings or whether the exhaustive lists of all possible strings, can help when searching or matching addresses in databases or text.
- Support parsing of all common MAC Address formats in usage
- Integration of MAC Address with IPv6
- Polymorphism in the code for IPv4 and IPv6 for applications which must support both transparently. You can write generic non-version-specific code to validate addresses, connect to addresses, print addresses, mask addresses, etc.
- Thread-safety and immutability. The core objects (host names, address strings, addresses, address sections, address segments) are all immutable (like java.lang.String or java.lang.Integer instances). They do not change their underlying value.
- Manipulation of addresses with prefixes, masks, sections, segments and subnetting: applying network prefixes, masking, splitting addresses into sections, joining address segments into larger segments, generating new subnets and supernets from existing addresses and subnets, iterating through subnets, checking containment within subnets, ipv4-ipv6 conversion, ipv6-mac conversion
- Sorting and comparison of host names, addresses, address strings and subnets
- Integrate with the java classes InetAddress, Inet6Address, Inet4Address.

## Supported IP Address Formats
This includes, those supported by the well-known routines inet_aton and inet_pton, the subnet formats listed above, all combinations of the above, and others:
- all the formats supported by inet_pton and inet_aton
- all the formats supported by nmap
- the subnet formats listed above, whether prefixed, masked, wildcards, ranges
- IPv6 canonical, compressed (1::1), mixed (1:2:3:4:5:6:1.2.3.4), [bracketed], and so on
- Hex values
- IPv6 base 85 values
- * represents all addresses both ipv4 and ipv6
- /x with no associated address is interpreted as the mask for prefix length x
- "" the empty string is considered the default loopback
For a more detailed list or formats parsed, some examples are below, or see the javadoc for IPAddressString.

Subnet formats
- CIDR (Classless Inter-Domain Routing) prefix length subnets
  Adding the prefix length /x creates the subnet for that network prefix length. The subnet 1.2.0.0/16 is the set of all addresses starting with 1.2
- Wildcard (* _) and range (-) subnets:
  * denotes all possible values in one or more segments, so 1.*.*.* or just 1.* is equivalent to 1.0.0.0/8
  0-1 denotes the range from 0 to 1
  _ replaces any digit at the end of a segment, for example 1_ represents 10 to 19 in decimal or 10 to 1f in hex
- Combinations:
  Applying a prefix length to a subnet simply applies the prefix to every element of the subnet. 1.*.0.0/16 is the same subnet of addresses as 1.0.0.0/8

For a more detailed list or formats parsed, some examples are below, or see the javadoc for IPAddressString.

## Core classes
The core classes are HostName, IPAddressString, and MACAddressString along with the Address base class and its subclasses IPAddress, IPv4Address, IPv6Address, and MACAddress. If you have a textual representation of an IP address, then start with HostName or IPAddressString. If you have numeric bytes or integers, then start with IPV4Address, IPV6Address or MACAddress. Note that address instances can represent either a single address or a subnet. If you have an address or host with a port, then use HostName.

## Parse String Representation of IP Address or Host Name
IPAddressString is used to convert. You can use one of getAddress or toAddress, the difference being whether parsing errors are handled by exception or not.

IPAddress address = new IPAddressString("1.2.3.4").getAddress();
if(address != null) {
//use address here
}

or

try {
IPAddress address = new IPAddressString("1.2.3.4").toAddress();
//use address here
} catch (AddressStringException e) {
String msg = e.getMessage();//detailed message indicating issue
}

If you have either a host name or an address, you can use HostName:

public static void main(String[] args) {
check(new HostName("[::1]"));
check(new HostName("*"));
check(new HostName("a.b.com"));
}

static void check(HostName host) {
if(host.isAddress()) {
System.out.println("address: " + host.asAddress().toCanonicalString());
} else if(host.isAddressString()) {
System.out.println("address string with ambiguous address: " +
host.asAddressString());
} else {
System.out.println("host name with labels: " +
 Arrays.asList(host.getNormalizedLabels()));
}
}

Output:

address: ::1
address string with ambiguous address: *
host name with labels: [a, b, com]

Format Examples

Many formats are supported. For instance, the address 1:2:3:0:0:6:: can be represented many ways as shown.

static void parse(String formats[]) {
for(String format : formats) {
System.out.println(new IPAddressString(format).getAddress());
}
}

static void parseHost(String formats[]) {
for(String format : formats) {
System.out.println(new HostName(format).getAddress());
}
}

public static void main(String[] args) {
String formats[] = {
"1:2:3:0:0:6::",
"1:2:3:0:0:6:0:0",
"1:2:3::6:0:0",
"0001:0002:0003:0000:0000:0006:0000:0000",
"1:2:3::6:0.0.0.0",
"1:2:3:0:0:6::",
"008JQWOV7O(=61h*;$LC",
"0x00010002000300000000000600000000"
};
parse(formats);
String hostFormats[] = {
"[1:2:3:0:0:6::]",
"[1:2:3:0:0:6:0:0]",
"[1:2:3::6:0:0]",
"[0001:0002:0003:0000:0000:0006:0000:0000]",
"[1:2:3::6:0.0.0.0]",
"[1:2:3:0:0:6::]",
"[008JQWOV7O(=61h*;$LC]",
"[0x00010002000300000000000600000000]",
"0.0.0.0.0.0.0.0.6.0.0.0.0.0.0.0.0.0.0.0.3.0.0.0.2.0.0.0.1.0.0.0.ip6.arpa",
"1-2-3-0-0-6-0-0.ipv6-literal.net"
};
parseHost(hostFormats);
}

Output:
1:2:3:0:0:6:0:0
1:2:3:0:0:6:0:0
1:2:3:0:0:6:0:0
1:2:3:0:0:6:0:0
1:2:3:0:0:6:0:0
1:2:3:0:0:6:0:0
1:2:3:0:0:6:0:0
1:2:3:0:0:6:0:0
1:2:3:0:0:6:0:0
1:2:3:0:0:6:0:0
1:2:3:0:0:6:0:0
1:2:3:0:0:6:0:0
1:2:3:0:0:6:0:0
1:2:3:0:0:6:0:0

Subnet strings are supported as well, using CIDR prefix notation or characters indicating range (‘-‘ for a specific range or ‘*’ for full range segments).

For instance, the subnet ffff::/104 can be represented many ways:

static void parse(String formats[]) {
for(String format : formats) {
System.out.println(new IPAddressString(format).getAddress().toPrefixedEquivalent());
}
}

static void parseHost(String formats[]) {
for(String format : formats) {
System.out.println(new HostName(format).getAddress().toPrefixedEquivalent());
}
}

public static void main(String[] args) {
String prefixedFormats[] = {
"ffff::/104",
"ffff:0:0:0:0:0:0:0/104",
"ffff:0000:0000:0000:0000:0000:0000:0000/104",
"ffff::/104",
"ffff::0.0.0.0/104",
"=q{+M|w0(OeO5^EGP660/104"
};
String rangeFormats[] = {
"ffff:0:0:0:0:0:0-ff:*",
"ffff::0-ff:*",
"ffff::0-ff:*",
"0xffff0000000000000000000000000000-0xffff0000000000000000000000ffffff"
};
parse(prefixedFormats);
parse(rangeFormats);
String hostFormats[] = {
"[ffff::]/104",
"[ffff:0:0:0:0:0:0:0]/104",
"[ffff:0000:0000:0000:0000:0000:0000:0000]/104",
"[ffff::]/104",
"[ffff::0.0.0.0]/104",
"[=q{+M|w0(OeO5^EGP660]/104",

"[ffff:0:0:0:0:0:0-ff:*]",
"[ffff::0-ff:*]",
"[ffff::0-ff:*]",
"[0xffff0000000000000000000000000000-0xffff0000000000000000000000ffffff]",

"*.*.*.*.*.*.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.f.f.f.f.ip6.arpa",
"ffff-0-0-0-0-0-0-0.ipv6-literal.net/104"
};
parseHost(hostFormats);
}

Output:
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104
ffff:0:0:0:0:0:0:0/104

Delimited Segments

The subnet formats allow you to specify ranges of values. However, if you wish to parse addresses in which values are delimited, then you can use the methods parseDelimitedSegments(String) and countDelimitedAddresses(String) in IPAddressString. parseDelimitedSegments will provide an iterator to traverse through the individual addresses.

For example, given "1,2.3.4,5.6" parseDelimitedSegments will iterate through "1.3.4.6", "1.3.5.6", "2.3.4.6" and "2.3.5.6". You can then construct IPAddressString instances from those individual strings for parsing.

Address or Host Name Validation Options

Validation options allow you to restrict the allowed formats, whether you wish to support just IPv4 or IPv6, or whether you wish to support just single addresses, or whether you wish to allow different variants.

For IP addresses, you have the class IPAddressStringParameters which can be passed into IPAddressString, and for host names you have the class HostNameParameters which can be passed into HostName.

You constrict validation options using the appropriate builder classes that are nested classes in the options classes. Here is an example constructing host options along with nested address options within:

HostNameParameters HOST_OPTIONS_EXAMPLE = new HostNameParameters.Builder().
allowEmpty(false).
setEmptyAsLoopback(false).
setNormalizeToLowercase(true).
allowBracketedIPv6(true).
allowBracketedIPv4(true).getAddressOptionsBuilder().
allowPrefix(true).
allowMask(true).
setRangeOptions(RangeParameters.WILDCARD_AND_RANGE).
allow_inet_aton(true).
allowEmpty(false).
setEmptyAsLoopback(false).
allowAll(false).
allowPrefixOnly(false).
getIPv4AddressParametersBuilder().
allowPrefixLengthLeadingZeros(true).
allowPrefixesBeyondAddressSize(false).
allowWildcardedSeparator(true).
getParentBuilder().getParentBuilder().toParams();

The default options used by the library are permissive and not restrictive.

Host Name or Address with Port
For an address or host with port, use HostName. IPv6 addresses with ports must appear as [ipv6Address]:port to resolve the ambiguity of the colon separator, consistent with RFC 2732, 3986, 4038 and other RFCs.
HostName hostName = new HostName("[::1]:80");
System.out.println("host: " + hostName.getHost() + " address: " + hostName.getAddress() + " port: " + hostName.getPort());
hostName = new HostName("localhost:80");
System.out.println("host: " + hostName.getHost() + " port: " + hostName.getPort());
hostName = new HostName("127.0.0.1:80");
System.out.println("host: " + hostName.getHost() + " address: " + hostName.getAddress() + " port: " + hostName.getPort());

Output:
host: 0:0:0:0:0:0:0:1 address: 0:0:0:0:0:0:0:1 port: 80
host: localhost port: 80
host: 127.0.0.1 address: 127.0.0.1 port: 80

IP Version Determination and IPv4/v6 Conversion
With an IPAddress or IPAddressString object, you can check the version with isIPv4() and isIPv6() and get the appropriate subclass with toIPv4() or toIPv6(). You can also make use of isIPv4Convertible() and isIPv6Convertible() to do further conversions if the address is IPv4 mapped, or you can use your own determination (IPv4 translated, 6to4, 6over4, IPv4 compatible, etc) of how to convert back and forth using IPAddressConverter.
IPAddressString str = new IPAddressString("::ffff:1.2.3.4");
if(str.isIPv6()) {
IPv6Address ipv6Address = str.getAddress().toIPv6();
System.out.println(ipv6Address.toMixedString());
if(ipv6Address.isIPv4Convertible()) {
IPv4Address ipv4Address = ipv6Address.toIPv4();
System.out.println(ipv4Address.toNormalizedString());
}
}
Output:

::ffff:1.2.3.4
1.2.3.4

Once you have an IPAddress instance, there are methods to convert to bytes, to sections, to subnets or network prefixes, to masks, to java.net.InetAddress, to different textual representations, and so on.

Prefixed Addresses and to/getHostAddress()
This library will parse CIDR prefix IP addresses such as 10.1.2.3/24.
When you have a prefixed address, like 10.1.2.3/24 which has the prefix length of 24, this notation may typically denote the single, distinct interface address 10.1.2.3 with the first 24 bits indicating the IPv4 block, or the the IPv4 block of 255 addresses which includes 10.1.2.3 (although typically the block would be denoted 10.1.2.0/24 with zeros outside the length of the prefix).
In this library 10.1.2.3/24 represents the IPv4 block (subnet) rather than just the single address 10.1.2.3 paired with its prefix length of 24. This avoids the inconsistency where 10.1.2.3/24 would be a single address, while the similar address with host portion zeroed, 10.1.2.0/24, would denote a set of 255 addresses, a heuristic commonly used by network administrators. In this library, any prefixed address denotes the address block.
However, there are cases when you'd want to extract the original individual address paired with the prefix. For that there are the methods getHostAddress or toHostAddress which will provide the original host address 10.1.2.3 when parsing 10.1.2.3/24. You can also extract only the prefix length by calling getNetworkPrefixLength() on the IPAddressString instance.

IPAddressString ipAddressString = new IPAddressString("10.1.2.3/24");
IPAddress address = ipAddressString.getAddress();
IPAddress hostAddress = ipAddressString.getHostAddress();
Integer prefixLength = ipAddressString.getNetworkPrefixLength();
System.out.println(address);
System.out.println(address.toCanonicalWildcardString());
System.out.println(hostAddress);
System.out.println(prefixLength);

Output:

10.1.2.0/24
10.1.2.*
10.1.2.3
24

In this library, 10.1.2.3/24 is equivalent to 10.1.2.* when it comes to equality or comparison. The prefix is stored in the address, so the former will be aware that it is "prefixed", printing strings that incorporate the prefix and providing the network section upon calls to getNetworkSection() in IPAddress. If you have the latter address with no prefix length, you can convert to the former using the method toPrefixedEquivalent() in IPAddress.

Parse Non-Segmented Addresses – Hex, Octal, IPv6 Base 85
Typically, the segments or other punctuation identify a string as a host name an IPv4 address or an IPv6 address. The parser will also parse single segment values or a range of single segment values.
In such cases, ambiguity between IPv4 and IPv6 is resolved by the number of digits in the string, as there is no segment separator. The number of digits is 32 for IPv6 hexadecimal, 20 for IPv6 base 85 (see RFC 1924), and 11 or less for IPv4, which can be octal, hexadecimal, or decimal. For IPv4, digits are presumed decimal unless preceded by 0x for hexadecimal or 0 for octal, as is consistent with the inet_aton routine. For IPv6, 32 digits are considered hexadecimal and the preceding 0x is optional.
IPAddressString ipAddressString = new IPAddressString("4)+k&C#VzJ4br>0wv%Yp");//base 85
IPAddress address = ipAddressString.getAddress();
System.out.println(address);

ipAddressString = new IPAddressString("108000000000000000080800200c417a");//hex IPv6
address = ipAddressString.getAddress();
System.out.println(address);

ipAddressString = new IPAddressString("0x01020304");//hex IPv4
address = ipAddressString.getAddress();
System.out.println(address);

ipAddressString = new IPAddressString("000100401404");//octal IPv4
address = ipAddressString.getAddress();
System.out.println(address);

Output:

1080:0:0:0:8:800:200c:417a
1080:0:0:0:8:800:200c:417a
1.2.3.4
1.2.3.4

Parse Special Host Names – Reverse DNS Host Name, IPv6 Literal UNC Host Name
A couple of standardized host formats are recognized, namely the reverse DNS host format, and the UNC IPv6 literal host format.
HostName hostName = new HostName("a.7.1.4.c.0.0.2.0.0.8.0.8.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.8.0.1.ip6.arpa");
System.out.println(hostName.asAddress());
hostName = new HostName("4.3.2.1.in-addr.arpa");
System.out.println(hostName.asAddress());
hostName = new HostName("1080-0-0-0-8-800-200c-417a.ipv6-literal.net");
System.out.println(hostName.asAddress());
Output:
1080:0:0:0:8:800:200c:417a
1.2.3.4
1080:0:0:0:8:800:200c:417a

A couple of methods in HostName are available as well:
public boolean isUNCIPv6Literal()
public boolean isReverseDNS()

Parse IPv6 Zone or Scope ID
The IPv6 zone or scope ID is recognized, denoted by the ‘%’ character. It can be retrieved by IPv6Address.getZone().
IPAddress addr = new IPAddressString("::%eth0").getAddress();
if(addr.isIPv6()) {
System.out.println(addr.toIPv6().getZone());
}

Output:
eth0

## Address Sections
Addresses can be broken up into sections, and reconstituted from sections. A section is a series of segments. You can get the section for the full address by calling getSection(), or you can get subsections by calling one of the variants, either getSection(int) or getSection(int, int), which return a subsection spanning the given indices. You can also get the segments in an address by calling getSegment(int) or one of the variants of getSegments, either on the address or on a section of the address.
You can also reconstitute an address from a section or array of segments using the appropriate address constructor, if your section or array of segments has the correct number of segments for the address type.

Host and Network Sections of IP Address
Use getHostSection() and getNetworkSection() to get the host and network sections of an IP address as indicated by prefix length.
IPAddress address = new IPAddressString("1.2.3.4").getAddress();
IPAddressSection network = address.getNetworkSection(16, true);
IPAddressSection host = address.getHostSection(16);
System.out.println(network.toCanonicalString());
System.out.println(host.toCanonicalString());

Output:
1.2/16
3.4
Once you have a section of an address, most of the same methods are available as those available with addresses themselves.

## IP Address Operations
There are various methods for obtaining masking, subnets, and so on.
The methods mask, maskNetwork, bitwiseOr, bitwiseOrNetwork, removePrefixLength, adjustPrefixBySegment, adjustPrefixLength, applyPrefixLength, and setPrefixLength allow you to apply and adjust prefix lengths and masks to addresses and subnets. When applying an operation to a subnet, the operation is applied to every member of the subnet, so the result must something be representable with contiguous ranges, or you will get AddressTypeException. For instance, masking the subnet block of 255 addresses 0.0.0.0/24 with 0.0.0.128 results in the two addresses 0.0.0.0 and 0.0.0.128 which is not contiguous. However, this will not happen when using standard masking and subnetting techniques typical with IPv4 and IPv6 routing.
The following code demonstrates how to get the lowest address in a prefixed subnet using any one of three methods: getLowest, mask, or removePrefixLength.
String addr = "1.2.3.4";
IPAddress address = new IPAddressString(addr).getAddress();
int prefixLength = 16;
IPAddress maskWithPrefixLength = new IPAddressString("/" + prefixLength).
getAddress(address.getIPVersion());

IPAddress mask = address.getNetwork().getNetworkMask(16, false);
System.out.println("mask with prefix length " + maskWithPrefixLength);
System.out.println("mask " + mask);

//mask
IPAddress maskedAddress = address.mask(mask);
System.out.println("address " + address + " masked " + maskedAddress);
IPAddress subnet = address.applyPrefixLength(prefixLength);
IPAddress maskedSubnet = subnet.mask(mask);
System.out.println("subnet " + subnet + " masked " + maskedSubnet);

//getLower
IPAddress lowestAddressInSubnet = subnet.getLower();
System.out.println("lowest in subnet " + lowestAddressInSubnet);
System.out.println(maskedAddress.equals(maskedSubnet));
System.out.println(maskedAddress.equals(lowestAddressInSubnet));

//removePrefixLength
IPAddress prefixRemoved = subnet.removePrefixLength(true);
System.out.println("prefix removed " + prefixRemoved);

Output:
mask with prefix length 255.255.0.0/16
mask 255.255.0.0
address 1.2.3.4 masked 1.2.0.0
subnet 1.2.0.0/16 masked 1.2.0.0
lowest in subnet 1.2.0.0
true
true
prefix removed 1.2.0.0

Polymorphism
Simply change the string "1.2.3.4" in the code above to an IPv6 address like "a:ffff:b:c:d::f" and the code all works the same.

Output:
mask with prefix length ffff::/16
mask ffff::
address a:ffff:b:c:d::f masked a::
subnet a::/16 masked a::
lowest in subnet a::
true
true

Handling Subnets and Network Prefixes
There are various additional methods for managing networks not listed above, such as:
- toPrefixedEquivalent: Converts an address with wildcards to an equivalent address with a prefix length. The resulting address will span the same range of values as the original.
- toMinPrefixedEquivalent: Converts an address to an equivalent address with the smallest possible prefix length. The resulting address will span the same range of values as the original.
- getMaskPrefixLength: Will return the prefix length for a network or host mask, or null otherwise
- append, prepend, replace: Add or replace segments in sections. To remove, use a variant of getSection
- adjustPrefixBySegment: Will create a larger network or smaller subnet address by increasing or decreasing the prefix length to the next segment boundary. If prefix length is increased, the additional prefix bits can be either zero or the full range of possible values.
- removePrefixLength, adjustPrefixLength, applyPrefixLength, setPrefixLength: Add, remove or adjust prefix lengths by the indicated values. There are variants to control whether extended prefix lengths have zeros for the added bits, or whether the bits remain full range. The default behavior when extending a prefix length is to insert zeros in the bits added to the prefix. The difference between applyPrefixLength and setPrefixLength is that the former does not shorten a prefix length; applyPrefixLength will not decrease the size of a subnet.
- mask, maskNetwork, bitwiseOr, bitwiseOrNetwork: apply masks to subnets and addresses. The network variants allow you to mask just the network portion and apply a prefix length, while the others remove any existing prefix length.
- reverseBits, reverseBytes, reverseBytesPerSegment, reverseSegments: useful for handling endianness (network byte order sometimes requires bytes be reversed), or DNS lookup, or other reasons for reversing bits and bytes.
- subtract: Computes the subnet difference, the set of addresses in the subnet but not in the argument subnet. Subtracts a given subnet from the receiver subnet, returning an array of subnets for the result.

Subnetting
Subnetting can be accomplished using various address manipulation methods. Given a prefixed IP address, you can extend the prefix length and insert bits for an extended prefix and new subnet of the previous address block, as shown in the following example.
int originalPrefix = 18, adjustment = 4;
IPAddress address = new IPAddressString("207.0.64.0").getAddress();
IPAddress address2 = address.setPrefixLength(originalPrefix);
IPAddress prefixExtension = new IPAddressString("0.0.4.0").getAddress();

IPAddress subnet1 = address2.adjustPrefixLength(adjustment);//extend the prefix length
System.out.println(subnet1);

IPAddress subnet2 = subnet1.bitwiseOrNetwork(prefixExtension, originalPrefix + adjustment); //adjust the extended prefix
System.out.println(subnet2);

Output:
207.0.64.0/18
207.0.64.0/22
207.0.68.0/22

Here is the same subnetting operation using segment replacement:
IPv4Address address = new IPAddressString("207.0.64.0/18").getAddress().toIPv4();
IPv4AddressSection replacementSection = new IPAddressString("0.0.68.0/22").getAddress().toIPv4().getSection(2);
IPAddress subnet = new IPv4Address(address.getSection().replace(replacementSection, 2));
System.out.println(subnet);

Output:
207.0.68.0/22

## Parse String Representation of MAC Address
Conversion is like IP address. MACAddressString is used to convert. You can use one of getAddress or toAddress, the difference being whether parsing errors are handled by exception or not.

MACAddress address = new MACAddressString("01:02:03:04:0a:0b").getAddress();
if(address != null) {
//use address here
}

or

try {
MACAddress address = new MACAddressString ("01:02:03:04:0a:0b").toAddress();
//use address here
} catch (AddressStringException e) {
String msg = e.getMessage();//detailed message indicating issue
}

Various Formats of MAC Addresses

MAC Addresses are expected to be in hexadecimal. However, there are a wide variety of accepted formats for MAC addresses:
aa:bb:cc:dd:ee:ff
aa-bb-cc-dd-ee-ff
aa bb cc dd ee ff
aabb.ccdd.eeff
aabbccddeeff
aabbcc-ddeeff

For the non-segmented format (aabbccddeeff), all 12 digits are required to avoid ambiguity. Additionally, MAC addresses can be either 48 or 64 bits, and so for each such format there is the 64-bit equivalent:
aa:bb:cc:dd:ee:ff:11:22
aa-bb-cc-dd-ee-ff-11-22
aa bb cc dd ee ff 11 22
aabb.ccdd.eeff.1122
aabbccddeeff1122
aabbcc-ddeeff1122

For the non-segmented 64-bit format (aabbccddeeff1122), all 16 digits are required to avoid ambiguity.

As with IP addresses, you can specify ranges using ‘*’ and ‘-’ like aa-bb:*:*:cc:dd:ee. The range character for addresses that use the dash ‘-’ character as a separator is ‘|’, like aa|bb-*-*-cc-dd-ee.

Format Examples

For instance, the address 0a:0b:0c:0d:0e:0f can be represented many ways:

static void parseMAC(String formats[]) {
for(String format : formats) {
System.out.println(new MACAddressString(format).getAddress());
}
}

public static void main(String[] args) {
String formats[] = {
"a:b:c:d:e:f",
"0a:0b:0c:0d:0e:0f",
"a:b:c:d:e:f",
"0a-0b-0c-0d-0e-0f",
"0a0b0c-0d0e0f",
"0a0b.0c0d.0e0f",
"0a 0b 0c 0d 0e 0f",
"0a0b0c0d0e0f"
};
parseMAC(formats);
}

Output:

0a:0b:0c:0d:0e:0f
0a:0b:0c:0d:0e:0f
0a:0b:0c:0d:0e:0f
0a:0b:0c:0d:0e:0f
0a:0b:0c:0d:0e:0f
0a:0b:0c:0d:0e:0f
0a:0b:0c:0d:0e:0f
0a:0b:0c:0d:0e:0f

Ranges can be specified in the same way as for IP addresses (‘-’ for a specific range or ‘*’ for full range segments).

For instance, the address range ff:0f:aa-ff:00-ff:00-ff:00-ff can be represented many ways:

static void parseMAC(String formats[]) {
for(String format : formats) {
System.out.println(new MACAddressString(format).getAddress());
}
}

public static void main(String[] args) {
String formats[] = {
"ff:f:aa-ff:00-ff:00-ff:00-ff",
"ff:f:aa-ff:*:*:*",
"ff:0f:aa-ff:*:*:*",
"ff-0f-aa|ff-*-*-*",
"ff0faa|ff0fff-*",
"ff0f.aa00-ffff.*",
"ff 0f aa-ff * * *",
"ff0faa000000-ff0fffffffff"
};
parseMAC(formats);
}

Output:
ff:0f:aa-ff:*:*:*
ff:0f:aa-ff:*:*:*
ff:0f:aa-ff:*:*:*
ff:0f:aa-ff:*:*:*
ff:0f:aa-ff:*:*:*
ff:0f:aa-ff:*:*:*
ff:0f:aa-ff:*:*:*
ff:0f:aa-ff:*:*:*

Delimited Segments

The range formats allow you to specify ranges of values. However, if you wish to parse addresses in which values are delimited, then you can use the methods parseDelimitedSegments(String) and countDelimitedAddresses(String) in MACAddressString. parseDelimitedSegments will provide an iterator to traverse through the individual addresses.

For example, given "1,2:3:4,5:6:7:8", countDelimitedAddresses will return 4 for the possible combinations: "1:3:4:6:7:8", "1:3:5:6:7:8", "2:3:4:6:7:8" and "2:3:5:6:7:8". With each string obtained from parseDelimitedSegments you can construct a MACAddressString instance.

MAC Address Validation Options

Validation options allow you to restrict the allowed formats.

You have the class MACAddressStringParameters which can be passed into MACAddressString

You constrict validation options using the appropriate builder classes that are nested classes in the options classes. Here is an example:

MACAddressStringParameters MAC_ADDRESS_OPTIONS_EXAMPLE = new MACAddressStringParameters.Builder().
allowEmpty(false).
allowAll(false).
getFormatBuilder().
setRangeOptions(RangeParameters.NO_RANGE).
allowLeadingZeros(true).
allowUnlimitedLeadingZeros(false).
allowWildcardedSeparator(false).
allowShortSegments(true).
getParentBuilder().
toParams();

The default options used by the library are permissive and not restrictive.

MAC Address Prefix Lengths

Prefix length in this library is defined general as the bit-length of the portion of the address that is not specific to an individual address but common amongst a group of addresses. For IP addresses, this is explicitly defined as part of the address using the ‘/’ character. For IP addresses, the prefix is potentially variable and depends on how subnets have been allocated.
MAC Addresses don’t have the exact same concept of prefix length as IP addresses. But concept of prefix can be applied in a more implicit sense. For instance, a MAC address is typically divided into an OUI (Organizationally Unique Identifier) and ODI (Organizational Defined Identifier), so you might consider the OUI bits as the prefix. There are other ways of assigning MAC address blocks as well, such as IAB (individual address block), or MA-S/MA-M/MA-L (MAC Address block small, medium, and large), in which a certain number of higher bits are provided as an identifier to organizations from which they can create various extended identifiers using the lower bits. There is generally a pre-defined set of high bits that can be considered a prefix. This prefix is not variable and was typically assigned by the IEEE. However, there is no explicit way to represent a MAC address with an associated prefix, so the prefix is implicit to the address when it is created.
Within this library, the prefix for a MAC address is defined as the largest number of high bits for which an address represents all addresses with the same set of higher bits.
For instance, the prefix length of aa:*:*:*:*:* is 8 because the address represents all addresses that start with the same 8 bits "aa". The prefix length of aa:*:cc:*:*:* is 24 because the address represents all addresses that start with the same 16 bits aa:*:cc. The address aa:bb:cc:dd:ee:ff does not have a prefix or prefix length as it represents just a single address.
This means that on the MAC side, the prefix length is implicit and based upon the address, while on the IP address side, the prefix length is explicitly defined.

## MAC Address Operations
Many of the same address operations available for IP addresses are available for MAC addresses, including the prefix operations (although prefixes have somewhat different meaning for MAC as described in the previous section of this document), the section and segment access methods, iterators, containment, and reversal of bits, bytes and segments.
The reverse operations are useful for for "MSB format", "IBM format", "Token-Ring format", and "non-canonical form", where the bits are reversed in each byte of a MAC address.

## IPv6 – MAC Address Integration
There is a standardized procedure for converting MAC addresses to IPv6 given a IPv6 64 bit prefix, as described in IETF RFC 2464, RFC 3513, and RFC 4944.
It details how to combine a 48 bit MAC address with a 64 bit IPv6 network prefix to produce a 128 bit IPv6 address. This is done by first constructing a 64-bit extended unique IPv6 interface identifier (EUI-64) from the MAC address. This library has implemented the same MAC / IPv6 integration in multiple ways.

Starting with a MAC address or section and with the IPv6 prefix, you can construct an IPv6 address.
public IPv6Address(IPv6Address prefix, MACAddress eui)
public IPv6Address(IPv6AddressSection section, MACAddress eui)
public IPv6Address(IPv6AddressSection section, MACAddressSection eui)
public IPv6Address(IPv6AddressSection section, MACAddressSection eui, CharSequence zone)

There are equivalent methods in the class MACAddress for producing the link local address which has a pre-defined prefix, or for producing the host (interface identifier) address section of an IPv6 address.
public IPv6Address toLinkLocalIPv6()
public IPv6AddressSection toEUI64IPv6()

There is a similar method in MACAddressSection
public IPv6AddressSection toEUI64IPv6()

A MAC address is either 48 or 64 bits. To be converted to IPv6, the 48 bit address has segments inserted (two 1 byte MAC segments with value 0xfffe) to extend the address to 64 bits. For a 64 bit MAC address to be convertible, those same two segments must match the expected value of 0xffe. The following methods in MACAddress check will 64 bit addresses to ensure that are compatible with IPv6 by checking that the value of those two segments matches 0xfffe. Note that the asMAC argument allows you to extend using 0xffff rather than 0xfffe which is another manner by which a 48 bit MAC address can be extended to 64 bits. However, for purposes of extending to an IPv6 address the argument should be false so that the EUI-64 format is used.
public boolean isEUI64(boolean asMAC)
public MACAddress toEUI64(boolean asMAC)

There are similar methods in MACAddressSection
public boolean isEUI64(boolean asMAC)
public boolean isEUI64(boolean asMAC, boolean partial)
public MACAddressSection toEUI64(boolean asMAC)

Given an existing EUI-64 section you can use the prepend and append methods to create a full IPv6 address section containing all segments:
public IPv6AddressSection prepend(IPv6AddressSection other)
public IPv6AddressSection append(IPv6AddressSection other)

and from there you just construct the address:
public IPv6Address(IPv6AddressSection section)

To go the reverse direction IPv6 to MAC, there is a method in IPv6Address to produce a MAC address:
public MACAddress toEUI(boolean extended)
and another in IPv6AddressSection that uses whatever part of the interface identifier is included in the section to produce a MAC address section:
public MACAddressSection toEUI(boolean extended)
For instance, if the IPV6 address section is the 8 bytes corresponding to the network prefix of an IPV6 address section, then the resulting MAC address section will be 0 bytes. If the IPV6 address section is the 8 bytes corresponding to the interface identifier, and that identifier has the required 0xfffe values in the 5th and 6th bytes, then the MAC address section will be the full 8 bytes of an EUI-64 MAC address.

The following code is an example of constructing IPv6 addresses from a MAC address:

public static void main(String args[]) {
MACAddressString macStr = new MACAddressString("aa:bb:cc:dd:ee:ff");
MACAddress macAddress = macStr.getAddress();
IPv6Address linkLocal = macAddress.toLinkLocalIPv6();
System.out.println(linkLocal);

IPAddressString ipv6Str = new IPAddressString("1111:2222:3333:4444::/64");
IPv6Address ipv6Address = ipv6Str.getAddress().toIPv6();
IPv6Address macIpv6 = new IPv6Address(ipv6Address, macAddress);
System.out.println(macIpv6);
}

Output:
fe80:0:0:0:a8bb:ccff:fedd:eeff
1111:2222:3333:4444:a8bb:ccff:fedd:eeff

## Address Framework
Much like there is a Java collections framework, there is an address framework to the IPAddress library. It is a unified set of inter-related interfaces, abstract implementations, and algorithms for all addresses and address components. It allows you to manipulate these items independently of implementation details, and provides standard interfaces to addresses and address components for code reuse and polymorphism. It represents the common structure of addresses, sections, segments, and so on.
You might wish to manipulate address components of different shapes and sizes transparently, or you may wish to manipulate different types of addresses or different address versions transparently. One element of the interface is the ability to convert any address component to bytes, whether division, segment, section, or address.
There is a hierarchy for the standard Address and Address Component data structures, which are addresses, sections of addresses, and segments of equal byte size inside those address sections.

There is a more diversified hierarchy for non-standard address structures, in which addresses or address sections might be divided into divisions of unequal length, or of non-integral bytesize.

The address hierarchy of interfaces (purple) and classes (green) is shown:

The full class hierarchy showing addresses, sections, division groupings, segments and divisions is shown here, separated into the three primary categories shown above. The dashed lines indicate there are a few less-prominent classes in the library not shown in the diagram.

## Conversion to String Representation of Address
AddressSegmentSeries objects (such as Address and AddressSection) have methods that produce strings in various formats: toCanonicalString, toNormalizedString, toCompressedString, and toHexString.

public static void main(String[] args) {
printStrings(new MACAddressString("a:bb:c:dd:e:ff").getAddress());
printStrings(new MACAddressString("a:bb:c:*").getAddress());
printStrings(new IPAddressString("a:bb:c::/64").getAddress());
printStrings(new IPAddressString("1.2.3.4").getAddress());
printStrings(new IPAddressString("1.2.3.4/16").getAddress());
printStrings(new IPAddressString("a:bb:c::dd:e:ff").getAddress());
}
static void printStrings(AddressSegmentSeries series) {
System.out.println(series.toCanonicalString());
System.out.println(series.toNormalizedString());
System.out.println(series.toCompressedString());
System.out.println(series.toHexString(true));
System.out.print("lower: " + series.getLower() + " bytes:");
System.out.println(Arrays.toString(series.getBytes()));
System.out.print("upper: " + series.getUpper() + " bytes:");
System.out.println(Arrays.toString(series.getUpperBytes()));
System.out.println();
}

Output:
0a-bb-0c-dd-0e-ff
0a:bb:0c:dd:0e:ff
a:bb:c:dd:e:ff
0x0abb0cdd0eff
lower: 0a:bb:0c:dd:0e:ff bytes:[10, -69, 12, -35, 14, -1]
upper: 0a:bb:0c:dd:0e:ff bytes:[10, -69, 12, -35, 14, -1]

0a-bb-0c-*-*-*
0a:bb:0c:*:*:*
a:bb:c:*:*:*
0x0abb0c000000-0x0abb0cffffff
lower: 0a:bb:0c:00:00:00 bytes:[10, -69, 12, 0, 0, 0]
upper: 0a:bb:0c:ff:ff:ff bytes:[10, -69, 12, -1, -1, -1]

a:bb:c::/64
a:bb:c:0:0:0:0:0/64
a:bb:c::/64
0x000a00bb000c00000000000000000000-0x000a00bb000c0000ffffffffffffffff
lower: a:bb:c:0:0:0:0:0 bytes:[0, 10, 0, -69, 0, 12, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0]
upper: a:bb:c:0:ffff:ffff:ffff:ffff bytes:[0, 10, 0, -69, 0, 12, 0, 0, -1, -1, -1, -1, -1, -1, -1, -1]

1.2.3.4
1.2.3.4
1.2.3.4
0x01020304
lower: 1.2.3.4 bytes:[1, 2, 3, 4]
upper: 1.2.3.4 bytes:[1, 2, 3, 4]

1.2.0.0/16
1.2.0.0/16
1.2.0.0/16
0x01020000-0x0102ffff
lower: 1.2.0.0 bytes:[1, 2, 0, 0]
upper: 1.2.255.255 bytes:[1, 2, -1, -1]

a:bb:c::dd:e:ff
a:bb:c:0:0:dd:e:ff
a:bb:c::dd:e:ff
0x000a00bb000c0000000000dd000e00ff
lower: a:bb:c:0:0:dd:e:ff bytes:[0, 10, 0, -69, 0, 12, 0, 0, 0, 0, 0, -35, 0, 14, 0, -1]
upper: a:bb:c:0:0:dd:e:ff bytes:[0, 10, 0, -69, 0, 12, 0, 0, 0, 0, 0, -35, 0, 14, 0, -1]

The IPAddress and IPAddressSection classes and their version-specific subclasses have additional methods to produce specific strings representing the address:

public static void main(String[] args) {
IPAddress address = new IPAddressString("a:b:c::e:f").getAddress();
print(address);
address = new IPAddressString("a:b:c::").getAddress();
print(address);
address = new IPAddressString("a:b:c:*::").getAddress();
print(address);
}

static void print(IPAddress address) {
System.out.println(address.toCanonicalString());
System.out.println(address.toFullString());
System.out.println(address.toNormalizedString());
System.out.println(address.toSQLWildcardString());
System.out.println(address.toSubnetString());
try {
if(address.isIPv6()) {
System.out.println(address.toIPv6().toMixedString());
System.out.println(address.toIPv6().toBase85String());//throws for a:b:c:*:: because the address cannot be represented as a range of two single values
}
System.out.println(address.toBinaryString());//throws for a:b:c:*:: because the address cannot be represented as a range of two single values
System.out.println(address.toHexString(true)); //throws for a:b:c:*:: because the address cannot be represented as a range of two single values
} catch(AddressTypeException e) {}
System.out.println();
}

Output:

a:b:c::e:f
000a:000b:000c:0000:0000:0000:000e:000f
a:b:c:0:0:0:e:f
a:b:c:0:0:0:e:f
a:b:c::e:f
a:b:c::0.14.0.15
00|N0s0$N0-%*(tF74+!
00000000000010100000000000001011000000000000110000000000000000000000000000000000000000000000000000000000000011100000000000001111
0x000a000b000c000000000000000e000f

a:b:c::
000a:000b:000c:0000:0000:0000:0000:0000
a:b:c:0:0:0:0:0
a:b:c:0:0:0:0:0
a:b:c::
a:b:c::
00|N0s0$N0-%*(tF5l-X
00000000000010100000000000001011000000000000110000000000000000000000000000000000000000000000000000000000000000000000000000000000
0x000a000b000c00000000000000000000

a:b:c:*::
000a:000b:000c:0000-ffff:0000:0000:0000:0000
a:b:c:*:0:0:0:0
a:b:c:%:0:0:0:0
a:b:c:*::
a:b:c:*::

IPv6 string methods

There are additional methods for Ipv6, the methods toMixedString() and toBase85String()

UNC Strings

The method toUNCHostName() produces the UNC IP-literal string.
IPAddressString ipAddressString = new IPAddressString("2001:db8::1");
IPAddress address = ipAddressString.getAddress();
System.out.println(address.toUNCHostName());

ipAddressString = new IPAddressString("1.2.3.4");
address = ipAddressString.getAddress();
System.out.println(address.toUNCHostName());

Output:
2001-db8-0-0-0-0-0-1.ipv6-literal.net
1.2.3.4

DNS Lookup Strings

The methods toReverseDNSLookupString() will produce a string for DNS lookup. If you wish to do a DNS lookup for a subnet rather than a full address, you can use getNetworkSection() to provide the network section you wish to lookup. You can specify the prefix length in either the string itself or the call to get the network section.

IPAddressString ipAddressString = new IPAddressString("2001:db8::1");
IPAddress address = ipAddressString.getAddress();
System.out.println(address.toReverseDNSLookupString());

IPAddressSection addressSection = address.getNetworkSection(64);
System.out.println(addressSection.toReverseDNSLookupString());

ipAddressString = new IPAddressString("2001:db8::1/64");
address = ipAddressString.getAddress();
System.out.println(address.toReverseDNSLookupString());

addressSection = address.getNetworkSection();
System.out.println(addressSection.toReverseDNSLookupString());

Output:
1.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.8.b.d.0.1.0.0.2.ip6.arpa
0.0.0.0.0.0.0.0.8.b.d.0.1.0.0.2.ip6.arpa
*.*.*.*.*.*.*.*.*.*.*.*.*.*.*.*.0.0.0.0.0.0.0.0.8.b.d.0.1.0.0.2.ip6.arpa
0.0.0.0.0.0.0.0.8.b.d.0.1.0.0.2.ip6.arpa

General String Methods

The methods toCanonicalString and toCompressedString are available for any address or address section.

The methods toHexString and toNormalizedString are available for any address component.

Avoiding Prefix Length Indicator in Strings

To choose to print wildcards '*' and range characters '-' as opposed to using prefix length, there are additional methods:

public static void main(String[] args) {
IPAddress address = new IPAddressString("a:b:c::/64").getAddress();
print(address);
address = new IPAddressString("a:b:c:*::/64").getAddress();
print(address);
}

static void print(IPAddress address) {
System.out.println(address.toCanonicalString());
System.out.println(address.toCanonicalWildcardString());
System.out.println(address.toFullString());
System.out.println(address.toNormalizedString());
System.out.println(address.toSQLWildcardString());
System.out.println();
}

Output:

a:b:c::/64
a:b:c:0:*:*:*:*
000a:000b:000c:0000:0000:0000:0000:0000/64
a:b:c:0:0:0:0:0/64
a:b:c:0:%:%:%:%

a:b:c:*::/64
a:b:c:*:*:*:*:*
000a:000b:000c:0000-ffff:0000:0000:0000:0000/64
a:b:c:*:0:0:0:0/64
a:b:c:%:%:%:%:%

IP Version-dependent Strings
Some strings are version-dependent:

public static void main(String[] args) {
//toSubnetString() prefers '*' for IPv4 and prefix for IPv6
System.out.println(new IPAddressString("1.2.0.0/16").getAddress().toSubnetString());
System.out.println(new IPAddressString("a:b::/64").getAddress().toSubnetString());

//converts IPv4-mapped to a:b:c:d:e:f:1.2.3.4 notation
System.out.println(new IPAddressString("::ffff:a:b").getAddress().toConvertedString());
}

Output:

1.2.*.*
a:b::/64
::ffff:0.10.0.11

Collections of IP Address Strings

Alternatively, you can produce collections of strings:

public static void main(String[] args) {
IPAddress address = new IPAddressString("a:b:c::e:f").getAddress();
print(address);
}

private static void print(IPAddress address) {
//print(address.toAllStrings()); produces many strings
print(address.toStandardStrings());
print(new String[] {""});
}

public static void print(String strings[]) {
for(String str : strings) {
System.out.println(str);
}
}

Output:

a:b:c:0:0:0:0.14.0.15
a:b:c:0:0:0:000.014.000.015
000a:000b:000c:0000:0000:0000:0.14.0.15
000a:000b:000c:0000:0000:0000:000.014.000.015
A:B:C:0:0:0:0.14.0.15
A:B:C:0:0:0:000.014.000.015
000A:000B:000C:0000:0000:0000:0.14.0.15
000A:000B:000C:0000:0000:0000:000.014.000.015
a:b:c::0.14.0.15
a:b:c::000.014.000.015
000a:000b:000c::0.14.0.15
000a:000b:000c::000.014.000.015
A:B:C::0.14.0.15
A:B:C::000.014.000.015
000A:000B:000C::0.14.0.15
000A:000B:000C::000.014.000.015
a:b:c:0:0:0:e:f
000a:000b:000c:0000:0000:0000:000e:000f
A:B:C:0:0:0:E:F
000A:000B:000C:0000:0000:0000:000E:000F
a:b:c::e:f
000a:000b:000c::000e:000f
A:B:C::E:F
000A:000B:000C::000E:000F

The String collections can be customized with toNormalizedString(StringOptions params)
Note that string collections never have duplicate strings. The String collections can be customized with toStrings(IPStringBuilderOptions options).

## Searching Text of Databases for all Addresses in a Subnet
Suppose you wanted to search for all addresses from a subnet in a large amount of text data. For instance, suppose you wanted to search for all addresses in the text from the subnet a:b:0:0::/64. You can start a representation of just the network prefix section of the address, then you can get all such strings for that prefix.
IPAddressSection prefix = new IPAddressString("a:b::").getAddress().
getNetworkSection(64, false);
String strings[] = prefix.toStandardStringCollection().toStrings();
for(String str : strings) {
System.out.println(str);
}

Output:
a:b:0:0
000a:000b:0000:0000
A:B:0:0
000A:000B:0000:0000
a:b::
000a:000b::
A:B::
000A:000B::

If you need to be more stringent or less stringent about the address formats you wish to search, then you can use toStringCollection(IPStringBuilderOptions options) with an instance of IPv6StringBuilderOptions.
Searching for those strings will find the subnet addresses. However, you may get a few false positives, like "a:b::d:e:f:a:b". To eliminate the false positives, you can just emulate in Java the SQL code produced below for the SQL database search, using substrings constructed from the segment separators.
For a MySQL database search:
public static void main(String[] args) {
IPAddressSection prefix = new IPAddressString("a:b::").
getAddress().getNetworkSection(64, false);
StringBuilder sql = new StringBuilder("Select rows from table where ");
prefix.getStartsWithSQLClause(sql, "column1");
System.out.println(sql);
}
Output:
Select rows from table where ((substring_index(column1,':',4) = 'a:b:0:0') OR ((substring_index(column1,':',3) = 'a:b:') AND (LENGTH (column1) - LENGTH(REPLACE(column1, ':', '')) <= 6)))

For IPv4, another way to search for a subnet like 1.2.0.0/16 would be to do a SELECT with the following string
public static void main(String[] args) {
String wildcardString = new IPAddressString("1.2.0.0/16").
getAddress().toSQLWildcardString();
System.out.println(wildcardString);
}

Output:

1.2.%.%

Then your SQL search string would be like:
Select rows from table where column1 like 1.2.%.%

## Containment and Subnet Membership
To check whether an IP address is contained by a subnet:
IPAddress address = new IPAddressString("1.2.0.0/16").getAddress();
System.out.println(address.contains(new IPAddressString("1.2.3.4").getAddress()));
System.out.println(address.contains(new IPAddressString("1.2.3.0/24").getAddress()));
System.out.println(address.contains(new IPAddressString("1.2.3.0/25").getAddress()));
System.out.println(address.contains(new IPAddressString("1.1.0.0").getAddress()));

Output:
true
true
true
false

The contains method is not restricted to IP addresses or IP address prefixed addresses. There is a contains method for every Address or AddressSection.

There is also an assortment of iterators for addresses, sections, and segments which represent multiple values. There is an iterator(), getLower() method and getUpper() method for every address component.

## DNS Resolution and URLs
If you have a string that can be a host or an address and you wish to resolve to an address, create a HostName and use HostName.toResolvedAddress(). If you wish to obtain a string representation to be part of a URL, use HostName.toNormalizedString().

## Sorting and Comparisons
Comparing and sorting can be useful for storing addresses in certain types of data structures. All of the core classes implement java.lang.Comparable. Different representations of the same address or subnet are considered equal. Different representations of the same set of addresses are considered equal. However, HostName instances, IPAddressString instances, and IPAddress instances are not equal even when representing the same address or subnet.

The library provides IPAddressComparator and some implementations for comparison purposes. IPAddress uses the subclass CountComparator. When comparing subnets, you can either emphasize the count of addresses, or you can emphasize the values of the lower or upper address represented by the subnet, and comparators are provided for those variations.

## Networks and Caches
The library provides singleton network objects for each address type. The network objects have methods for obtaining masks and loopbacks. The networks also provide creator objects that create addresses, sections, and segments, and they perform caching of these address components for efficient memory usage and performance.
The network() methods in IPv4Address, IPv6Address, and MACAddress provide access to the respective network objects. Each network has an associated address creator object accessible from getAddressCreator() providing methods for address component creation that make use of the aforementioned caches.
If you wished to use your own subclasses of the address classes, you could also use your own network object, and your own address creator object, by replacing the network field of the respective address class that you have subclassed, and optionally the createAddressCreator method in the network class. That would allow you to control which types are created within the IP address library.
The IPAddressNetwork class defines IPAddressStringCache and HostNameCache. These cache classes allow you to cache identifier strings. Note that identifier strings will cache their associated addresses, whether parsed or resolved. Also note that addresses cache their associated strings and various other objects. Therefore, these cache classes go a long way towards allowing you to avoid creating the same objects and running the same code frequently. These caches do quick lookups using either bytes or strings, which might be ideal for some applications that handle many addresses or host names.